## Slide 1: How to set up your Raspberry Pi & Camera

## Slide 2: Components
Raspberry Pi Type B €32.50
Raspberry Pi Camera module €20.04
Edimax Wifi USB Adapter €11.19
Raspberry Pi Case €4.99
Camera Case €3.64
Power Supply €6.49
Shipping/Tax €16.26
Total: €95.11

## Slide 3: Components
SD card (minimum 2GB)
Keyboard
Ethernet Cable
HDMI Cable
HDMI Monitor/TV

## Slide 4: Setup
Download Arch Linux from;
  http://archlinuxarm.org/platforms/armv6/raspberry-pi
Use dd to copy to SD card
Resize to full size using gparted
Login in locally (or over ssh?) with root/root
CHANGE ROOT PASSWORD IMMEDIATELY:
  passwd
Update the hostname
  nano /etc/hostname

## Slide 5: Setup
Add your own user account
  useradd -m -g users -s /bin/bash thomas
  chfn thomas
  passwd thomas
Update package manager and install
  pacman -Syy
  pacman -S htop fail2ban cmake base-devel opencv ssmtp
If the install freezes use top to find out if update-mime-database is running
  killall update-mime-database

## Slide 6: Setup Mail
Gmail SMTP is easiest
nano /etc/ssmtp/ssmtp.conf
  root=youremail@gmail.com
  mailhub=smtp.gmail.com:587
  hostname=youremail@gmail.com
  UseSTARTTLS=Yes
  AuthUser=youremail
  AuthPass=yourpassword
  FromLineOverride=yes

## Slide 7: Setup Mail
chmod 640 /etc/ssmtp/ssmtp.conf
chown root:mail /etc/ssmtp/ssmtp.conf
gpasswd -a thomas mail
To send:
  echo -e "To: thelucid@gmail.com\nSubject: Test Message\n\nHello" > msg.txt
  ssmtp -s thelucid@gmail.com < msg.txt
  rm msg.txt

## Slide 8: Setup Camera
chmod 777 -R /opt/vc
nano /boot/config.txt
  gpu_mem=128
  start_file=start_x.elf
  fixup_file=fixup_x.dat
add export PATH=/opt/vc/bin:$PATH to /home/thomas/.bashrc
reboot

## Slide 9: Camera Source Code
Download zip from https://github.com/raspberrypi/userland
Extract to /opt/vc/userland
cd /opt/vc
sed -i 's/if (DEFINED CMAKE_TOOLCHAIN_FILE)/if (NOT DEFINED CMAKE_TOOLCHAIN_FILE)/g' makefiles/cmake/arm-linux.cmake

## Slide 10: Camera Source Code
mkdir build
cd build
cmake -DCMAKE_BUILD_TYPE=Release ..
make
make install
chmod 777 -R /opt/vc/userland
Now the bundled camera utility sources are compiled locally

## Slide 11: My Source Code
To run mkdir ~/cam
download source code, extract to ~/cam/src
mkdir ~/cam/build
cd ~/cam/build
cmake ../src
make
./run.sh

## Slide 12: Bash version
What’s going on here?
  Use built in raspiyuv to take 3 photos over 1 second
  Use unix cmp to print out bytewise differences
  Use unix awk to sum absolute differences
  If above a threshold, start recording with raspvid

## Slide 13: Bash version: The reality
Much slower
A lot more false positives
    Less control over frame grabbing
    Warm up/auto exposure unreliable
Bottom line
  C prevails

## Slide 14: End
Lots of help from http://thinkrpi.wordpress.com/2013/05/22/opencv-and-camera-board-csi/